## Slide 1
COMPUTER NETWORKS | B.TECH PRESENTATION
Building a Secure Campus
Wireless Network (WLAN)
with WPA2-Enterprise
Presented by: Your Name | Course: B.Tech CSE / IT | Subject: Computer Networks

## Slide 2
Introduction to Wireless Networks (WLAN)
What is a WLAN and how does it work?
What is WLAN?
A Wireless Local Area Network (WLAN) connects devices like laptops, phones, and tablets without physical cables — using radio waves.
How It Works
Data is sent through radio frequencies (2.4 GHz / 5 GHz). Access Points (APs) broadcast Wi-Fi signals that devices connect to.
IEEE Standard
Wi-Fi follows the IEEE 802.11 standard. Common versions: 802.11n, 802.11ac (Wi-Fi 5), 802.11ax (Wi-Fi 6).
📡 Campus WLANs can span multiple buildings and serve thousands of users simultaneously.

## Slide 3
What is Network Security & Why It Matters
Protecting data, users, and systems from threats
Network Security
A set of rules, technologies, and practices that protect a network from unauthorized access, misuse, and attacks. It ensures data confidentiality, integrity, and availability.
Common Threats on Campus Wi-Fi
Eavesdropping (packet sniffing)
Man-in-the-Middle attacks
Rogue Access Points (Evil Twin)
Unauthorized network access
The CIA Triad of Security
Confidentiality
Only authorized users can read data
Integrity
Data is not altered during transmission
Availability
Network is accessible when needed

## Slide 4
Overview of WPA2-Enterprise
The gold standard for secure Wi-Fi authentication
WPA2 (Wi-Fi Protected Access 2) — Enterprise Mode
A wireless security protocol that uses individual credentials per user (not a shared password) and a central authentication server to verify identity before granting network access.
AES Encryption
Uses 128/256-bit AES to encrypt all wireless traffic — virtually unbreakable.
802.1X Auth
Port-based authentication using EAP protocols (PEAP, EAP-TLS) for every user.
RADIUS Server
Central server manages all user credentials, policies, and access decisions.
Per-User Keys
Every session gets a unique encryption key — even if one is compromised, others stay safe.
Used by: MIT, Google, IIT Bombay, large enterprises worldwide

## Slide 5
WPA2-Personal vs WPA2-Enterprise
Choosing the right security model
WPA2-Personal (PSK)
Feature
WPA2-Enterprise (802.1X)
Single shared password
Authentication
Unique credentials per user
None (shared key)
User Identity
Individual login tracked
Home / Small office
Best For
Universities / Enterprises
Lower
Security Level
Much Higher
Easy
Setup
Requires RADIUS server
Not tracked
Audit Logs
Full user activity logs
Risk: if PSK leaks, all exposed
Key Risk
Risk: server misconfiguration
✅ For any campus with 50+ users, WPA2-Enterprise is strongly recommended.

## Slide 6
Key Components of WPA2-Enterprise
The three pillars of the system
RADIUS Server
Authentication Hub
RADIUS = Remote Authentication Dial-In User Service
Stores usernames, passwords & certificates
Accepts or rejects login requests
Example: FreeRADIUS (open-source), Cisco ISE
Communicates with APs using UDP port 1812
Access Points (APs)
Network Entry Nodes
Hardware devices that broadcast the Wi-Fi signal
Act as middleman between user device and RADIUS
Support 802.1X port-based authentication
Examples: Cisco Meraki, Ubiquiti UniFi, Aruba
Can handle 30–250 concurrent users each
Authentication Server
Identity Verifier
Validates user credentials (ID + Password or Certificate)
Integrated with LDAP / Active Directory
Issues session keys after successful auth
Logs every login attempt with timestamp
Can enforce device-level policies (e.g., OS type)

## Slide 7
Working Process — Authentication Flow (802.1X)
Step-by-step: How a user connects to the network
1
Association Request
User device sends request to connect to the AP
2
EAP Start
AP challenges the device with an EAP identity request
3
Identity Sent
Device sends username/certificate to AP
4
RADIUS Forwarded
AP forwards credentials to the RADIUS server
5
RADIUS Validates
RADIUS checks credentials against user database
6
Access Granted
RADIUS sends Accept + session key to AP → user is online
Protocol: EAP (Extensible Authentication Protocol) carried over 802.1X | Common EAP types: PEAP, EAP-TLS, EAP-TTLS

## Slide 8
Campus Network Architecture Diagram
How all components connect in a university environment
Internet
Firewall
Core Switch
RADIUS
Server
AP
Library
AP
Classroom
AP
Hostel
Distribution Switch
Laptop
Phone
Tablet
Legend:
Wired Connection
RADIUS Auth (dashed)
Wireless Connection

## Slide 9
Step-by-Step Implementation Guide
Setting up WPA2-Enterprise on a campus network
01
Install RADIUS Server
Install FreeRADIUS on a Linux server (Ubuntu). Configure radiusd.conf with network settings.
02
Configure Access Points
Set each AP to WPA2-Enterprise mode. Enter RADIUS server IP, port (1812), and shared secret.
03
Set Up User Database
Create user accounts in LDAP or Active Directory. Link RADIUS to the directory for credential lookup.
04
Create Certificates
Generate SSL/TLS certificates using OpenSSL. Deploy CA certificate to all user devices for server verification.
05
Configure EAP Method
Choose EAP-PEAP (easier) or EAP-TLS (stronger). Configure eap.conf on the RADIUS server.
06
Test & Monitor
Use tools like Wireshark to verify encrypted traffic. Monitor RADIUS logs for failed auth attempts.
Tools: FreeRADIUS · OpenSSL · Cisco Meraki Dashboard · Wireshark · Active Directory

## Slide 10
Security Benefits of WPA2-Enterprise
Why enterprises and universities prefer this standard
Strong Encryption
AES-CCMP 128/256-bit encryption
Session keys generated per user
Even captured packets are useless without key
Individual Authentication
Every user has unique login credentials
Compromised account doesn't affect others
Multi-factor auth (MFA) can be added
Access Control
Role-based access (student vs staff)
Restrict access by device type or OS
VLAN assignment based on user role
Audit & Visibility
Full log of who connected, when, for how long
Detect suspicious behavior in real time
Essential for compliance (GDPR, ISO 27001)

## Slide 11
Challenges & Limitations
What to be aware of before deployment
High
Complex Setup
Requires technical expertise to configure RADIUS, certificates, and LDAP integration.
Medium
Cost
Enterprise APs (Cisco, Aruba) and RADIUS infrastructure can be expensive for small institutions.
High
Certificate Management
Digital certificates expire and must be renewed. Improper management leads to connectivity issues.
Medium
Scalability
RADIUS server can become a bottleneck with thousands of concurrent users if not clustered.
Medium
Device Compatibility
Older devices or IoT devices may not support 802.1X or EAP methods, causing connection failures.
Low
User Experience
First-time setup on user devices (installing CA cert) can confuse non-technical users.

## Slide 12
Best Practices for Secure WLAN Deployment
Proven guidelines to maximize security and reliability
Use Strong Credentials
Enforce password complexity (12+ chars, symbols). Prefer EAP-TLS with certificates over PEAP with passwords.
Keep Certificates Valid
Automate certificate renewal (use Let's Encrypt or internal PKI). Alert admins 30 days before expiry.
Regular Firmware Updates
Update AP firmware and RADIUS software monthly. Patch known CVE vulnerabilities immediately.
Enable Audit Logging
Log all authentication events. Set up alerts for repeated failed logins (brute force detection).
Network Segmentation
Assign separate VLANs for students, faculty, IoT devices. Limit inter-VLAN traffic with ACLs.
Implement MFA
Add a second factor (OTP via email/SMS) for privileged users like admins and staff.

## Slide 13
Real-Life Example — eduroam Network
How universities worldwide implement WPA2-Enterprise
eduroam — Education Roaming
A global Wi-Fi roaming service used by 10,000+ universities in 100+ countries. When a student from IIT visits MIT, they can connect to Wi-Fi using their home university credentials — all secured with WPA2-Enterprise and 802.1X.
10,000+
Universities
100+
Countries
50M+
Users
WPA2-E
Security Standard
Indian Example: IIT Bombay
Uses WPA2-Enterprise with LDAP-backed RADIUS. Students authenticate with LDAP credentials. Guest VLAN provided for visitors.
Corporate Example: Google
Employees connect to 'Google WiFi' using their Google Workspace credentials. Certificate-based EAP-TLS used for managed devices.

## Slide 14
Future Scope — Beyond WPA2-Enterprise
Next-generation wireless security trends
WPA3-Enterprise
Released 2018
192-bit security mode (CNSA suite)
Simultaneous Authentication of Equals (SAE)
Eliminates offline dictionary attacks
Mandatory for Wi-Fi CERTIFIED WPA3 devices
Wi-Fi 6E & 7
Emerging Now
6 GHz band — less interference, higher speed
Multi-Link Operation (Wi-Fi 7) for reliability
OFDMA improves dense campus performance
Target Wakeup Time — great for IoT devices
Zero Trust Security
Trend 2024+
Never trust, always verify — even on internal network
Continuous device health checks during session
Micro-segmentation replaces VLAN-only isolation
AI-driven anomaly detection in real time
AI-Powered Security
Future Ready
Machine learning detects rogue APs automatically
Behavioral analytics catch insider threats
Auto-remediation: block suspicious device instantly
Predictive capacity planning for campus networks

## Slide 15
CONCLUSION
Key Takeaways
01
WPA2-Enterprise is the most secure Wi-Fi standard for multi-user environments like campuses.
02
It uses 802.1X, EAP, and RADIUS to authenticate each user individually with strong encryption.
03
Key components — RADIUS Server, Access Points, and Authentication Server — work together seamlessly.
04
Real-world adoption (eduroam, IIT, Google) proves its effectiveness and scalability.
05
The future lies in WPA3, Zero Trust, and AI-driven security — building on WPA2-Enterprise foundations.
Thank You | Questions Welcome | Building a Secure Campus WLAN with WPA2-Enterprise